## Slide 1: MIPS Instruction Encoding

## Slide 2: Why Fixed-Width Encoding?
Every MIPS instruction is exactly 32 bits. Decode logic is simpler, fetch is aligned, branch targets are predictable. The trade-off is code density — CISC architectures like x86 pack more work into fewer bytes.

## Slide 3: Three Instruction Formats
MIPS uses exactly three formats, distinguished by the top 6 bits (opcode). Everything else is a field layout negotiation.

## Slide 4: R-type Layout
Register-only instructions: add, sub, and, or, sll, jr, and so on.
| opcode(6) | rs(5) | rt(5) | rd(5) | shamt(5) | funct(6) |
All R-type instructions share opcode = 0x00; the funct field selects the actual ALU operation.

## Slide 5: R-type Example: add $t0, $t1, $t2
opcode = 000000
rs = 01001 (t1 = 9)
rt = 01010 (t2 = 10)
rd = 01000 (t0 = 8)
shamt = 00000
funct = 100000 (ADD)
Full word: 0x012A4020.

## Slide 6: I-type Layout
Immediate, loads, stores, branches: addi, lw, sw, beq, lui.
| opcode(6) | rs(5) | rt(5) | immediate(16) |
The 16-bit immediate is sign-extended for arithmetic and branches, zero-extended for logical ops.

## Slide 7: I-type Example: lw sp)
opcode = 100011 (LW)
rs = 11101 (sp = 29)
rt = 01000 (t0 = 8)
imm = 0x0004

## Slide 8: Branches Are PC-Relative
target = (PC + 4) + (sign_extend(imm) << 2)
Shifting by 2 gives a 128 KB branch range. The + 4 is because PC has already incremented by the time the branch executes.

## Slide 9: J-type Layout
Unconditional jumps: j, jal.
| opcode(6) | address(26) |

## Slide 10: Pseudo-Direct Addressing
target = { PC[31:28], address << 2 }
The low 2 bits are zero (word-aligned), and the top 4 bits come from the current PC — so j cannot cross a 256 MB region.

## Slide 11: Decoding in Hardware
A 6-bit opcode decoder steers the instruction into the right path. opcode == 0 routes to the funct-based R-type decoder. opcode == 2 || opcode == 3 selects J-type. Everything else is I-type.

## Slide 12: Sign-Extension Matters
addiu $t0, $t1, 0xFFFF does not add 65535 — the immediate is sign-extended to 0xFFFFFFFF, so it subtracts 1. Watch this on exam questions.

## Slide 13: Assembler Pseudo-instructions
The assembler expands friendly syntax into real encodings:
li $t0, 0x12345678 → lui $t0, 0x1234 + ori $t0, $t0, 0x5678
move $t0, $t1 → add $t0, $zero, $t1
blt $t0, $t1, L → slt $at, $t0, $t1 + bne $at, $zero, L

## Slide 14: Practice
Hand-encode these into hex. Bring your work to lab.
sub $s0, $s1, $s2
sw $t0, -8($fp)
j 0x00400100